Microcomputer-Controlled Car
Reference Manual
Version 1.0
Last Updated ???????
Table of Contents

Chapter 1: Overview

This is the microcomputer-controlled car project. This project's purpose is to make available an inexpensive test platform for ground vehicle control algorithms. Following are the major components of this project:
- 1 x RC racing car (AE Team Associated SC10)
- 1 x Raspberry Pi Model B microcomputer (revision 1 or 2)
- 1 x Arduino Pro Mini 5V 16MHz microcontroller
- 1 x Adadafruit 16 Channel 12-bit PWM/Serbo Driver – I2C Interface – PCA9685
- Custom software for the Arduino written in the Arduino C-like language
- Custom software for the Raspberry Pi written in Python
- Custom 5V power regulation circuitry

Chapter 2: RC Car

The RC racing car that was selected for this project is the AE Team Associated SC10, a 1:10 scale, ready-to-run 2WD, electric off road race truck. The stock car consists of the following major components:
- Independent suspension for the front and rear wheels
- 1 x Servo (XP DS1903MG) that steers the front wheels
- 1 x Radio Receiver 4 Channel 2.4GHz (XP TRS403-ssi)
- 1x Radio Transmitter (XP 2G 29215) 2.4GHz
- 1x Motor Controller (XP SC200)
- 1 x Ni-MH Battery Pack 7.2V 3600mAh
The servo, radio receiver, and motor controller are all compatible with 5V logic, though it is important to note that the motor controller must receive power